## Slide 1: DCSP-4: Fourier Transform
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2
Coding
Ls(X) > H(X)
Data transmission
Channel characteristics,
Signaling methods (ADC)
Interference and noise
Fourier transform
Data compression and encryption

## Slide 3
Bandwidth
The range of frequencies occupied by the signal is called its bandwidth.
0 B Frequency
Power

## Slide 4
The ADC process is governed by an important la
(will be discussed in Chapter 3)
An analogue signal of bandwidth B can be completely recreated from its sampled form provided its sampled at a rate equal to at least twice it bandwidth.
That is
S > 2 B
Nyquist-Shannon Theorem

## Slide 5: Example
I will guess that B = 1 Hz
Sample at 2B = 2 Hz: x[n] = [ 0 0 0 0 ]
Intuitively, I would say it will not work

## Slide 6: Example
I will guess that B = 1 Hz
Sample at 2B < 4 Hz: x[n] = [ 1 0 -1 0 1 0 -1 0 ]
According to N-S Thm, we can fully recover the original signal

## Slide 7: Example
I will guess that B = 1 Hz
Sample at 2B < 4 Hz: x[n] = [ 1 0 -1 0 1 0 -1 0 ]
According to N-S Thm, we can fully recover the original signal
Well, the blue line has the identical frequency, and x[n]. What is wrong?

## Slide 8: Noise in a channel

## Slide 9: Noise in a channel
Attenuation

## Slide 10: Noise in a channel

## Slide 11
Noise in a channel

## Slide 12: Noise in a channel

## Slide 13
Noise therefore places a limit on the channel at which we can transfer information
Obviously, what really matters is the signal to noise ratio (SNR).
This is defined by the ratio signal power S to noise power N, and is often expressed in deciBels (dB):
SNR=10 log10 (S/N) dB
SNR

## Slide 14: Noise sources
Input noise is common in low frequency circuits and arises from electric fields generated by electrical switching.
It appears as bursts at the receiver, and when present can have a catastrophic effect due to its large power.
Other peoples signals can generate noise: cross-talk is the term give to the pick-up of radiated signals from adjacent cabling.

## Slide 15: Noise sources
When radio links are used, interference from other transmitters can be problematic.
Thermal noise is always present. It is due to the random motion of electric charges present in all media. It can be generated externally, or internally at the receiver.
How to tell signal from noise?

## Slide 16: Communication Techniques I
Time frequency
Fourier Transform
bandwidth
noise power

## Slide 17: Communication Techniques I
Time frequency
Fourier Transform
bandwidth
noise power

## Slide 18: Communication Techniques II
Time, frequency and bandwidth
We can describe a signal in two ways.
The
One way is to describe its evolution in time domain,
as we usually do.
The other way is to describe its frequency content,
in frequency domain: what we will learn

## Slide 19: Your heartbeat
Ingredients: a frequency ω (units: radians)
an initial phase φ (units: radians) an amplitude A (units depending on underlying measurement)
a trigonometric function
e.g. x[n]= A cos(ωn+φ)
cosine wave, x(t), has a single frequency,
w =2 p/T
where T is the period i.e. x(t+T)=x(t).

## Slide 20: What do we expect?
Fre
Time
1 Hz
Power

## Slide 21: What do we expect?
Fre
Time
1 Hz
Power

## Slide 22: What do we expect?
Fre
Time
1 Hz
Power

## Slide 23: What do we expect?
Fre
Time
1 Hz
Power

## Slide 24: What do we expect?
Fre
Time
1 Hz
Power

## Slide 25
This representation is quite general.
In fact we have the following theorem due to Fourier.
Any signal x(t) of period T can be
represented as the sum of a set of
cosinusoidal and sinusoidal waves of
different frequencies and phases
Fourier Transform I

## Slide 26
In mathematics, the continuous Fourier transform is one of the specific forms of Fourier analysis.
As such, it transforms one function into another, which is called the frequency domain representation of the original function (which is often a function in the time-domain).
In this specific case, both domains are continuous and unbounded.
The term Fourier transform can refer to either the frequency domain representation of a function or to the process/formula that "transforms" one function into the other.
Fourier Transform II

## Slide 27: Fourier Transform III

## Slide 28
Continuous time (analogous signals): FT (Fourier transform)
it is in theory (in Warwick, we need it)
Discrete time: DTFT (infinity digital signals)
it is in theory (discrete version)
DFT: Discrete Fourier transform (finite digital signals
what we can use, one line in Matlab (fft))
Fourier Transform IV

## Slide 29: History of FT I
Gauss computes trigonometric series efficiently in 1805
Fourier invents Fourier series in 1807
People start computing Fourier series, and develop tricks Good comes up with an algorithm in 1958
Cooley and Tukey (re)-discover the fast Fourier transform algorithm in 1965 for N a power of a prime
Winograd combined all methods to give the most efficient FFTs

## Slide 30: Gauss
History of FT II

## Slide 31: Fourier
History of FT III

## Slide 32: Jianfeng Feng
History of FT IV

## Slide 33: History of FT V
Prof Feng

## Slide 34
Complex Numbers

## Slide 35: Exp(j a) = cos a + j sin a
Euler Formular

## Slide 36: The complex eponential
the trigonometric function of choice in DSP is the complex exponential:
x[n] = Aexp(j(ωn+φ))
= A[cos(ωn + φ) + j sin(ωn + φ)]

## Slide 37
The complex eponential

## Slide 38: Most beautiful Math Formula
exp ( j π ) + 1 = 0
Where e is Euler's number
J is the imaginary unit

## Slide 39: Fourier's Song

## Slide 40: Example
FT
IFT
Frequency-space
k2
k1
Image space
y
x

## Slide 42
Fun: Decoding dream (Horikawa et al. Science, 2013)

## Slide 43: Fun