## Slide 1: DCSP-5: Fourier Transform II
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2
This representation is quite general.
In fact we have the following theorem due to Fourier.
Any signal x(t) of period T can be represented as the sum of a set of cosinusoidal and sinusoidal waves of different frequencies
Fourier Theorem

## Slide 3: Today and next week summary
Introduce FT in layman’s language (today)
Applications (next week)

## Slide 4: This week’s summary
Introduce FT in layman’s language (today)
Applications (tomorrow)
You might find the world is different !

## Slide 5: summary
Introduce FT in layman’s language (today)
Talk about continuous FT since it is clean and simple
Come back to it on how to numerically calculate it later on
Intuition
Fourier theorem
Examples
Bandwidth

## Slide 6: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases
where A0 is the d.c. term, and T is the period of the waveform.

## Slide 7: Intuition of FT
Two dimensional space (all points)

## Slide 8: Intuition of FT
Two dimensional space (all points)
Two bases which are orthogonal
(1,0) (0,1)

## Slide 9: Intuition of FT
Two dimensional space (all points)
(a, b) = a (1,0) + b (0,1)
First basis second basis
a: the contribution from the first basis, the load at the first basis
b:

## Slide 10: Intuition of FT
Two dimensional space (all points)
(a, b) = a (1,0) + b (0,1)

## Slide 11: Intuition of FT
Two dimensional space (all points)
(a, b) = a (1,0) + b (0,1)
Signal space (all functions of t)
x (t) = a sin(ω t) + b sin (2 ω t)

## Slide 12: Intuition of FT
Two a point in it
(a, b) = a (1,0) + b (0,1)

## Slide 13: Intuition of FT
Two a point in it
(a, b) = a (1,0) + b (0,1)
Signal = coef basis coef basis

## Slide 14: Intuition of FT
Two a point in it
(a, b) = a (1,0) + b (0,1)
x(t) = ?
Signal = coef basis coef basis

## Slide 15: Intuition of FT
Two a point in it
(a, b) = a (1,0) + b (0,1)
x(t) = a F1(t) +b F2(t)
Signal = coef basis coef basis

## Slide 16: Intuition of FT
It is a branch of mathematics called
functional analysis: treat each function as a point in a functional space
It is the starting pointe of modern mathematics
It is also the actual power of mathematics
Branch space, Hilbert space etc.

## Slide 17: Intuition of FT
How to calculate these coefficients?
o
(a, b) = a (1,0) + b (0,1)
Functional
x (t) = a cos(ω t) + b cos (2 ω t)
w = 2 pi /T

## Slide 18: Intuition of FT
Coefficient is obtained via Inner product
<(x, y), (m,n)> = xm+yn
All bases are orthogonal
<(0, 1), (1,0)> = 0, (0,1) (1, 0)
(a, b) = a (1,0) + b (0,1)
Therefore
<(a, b), (1,0)> = a <(1,0), (1,0)> + b <(0,1), (1,0)> = a
<(a, b), (0,1)> = a <(1,0), (0,1)> + b <(0,1), (0,1)> = b

## Slide 19: Intuition of FT
Two dimensi coefficient is obtained via Inner product
(a, b) = a (1,0) + b (0,1)
<(a, b), (1,0)> = a <(1,0), (1,0)> + b <(0,1), (1,0)> = a
Functional coefficient is obtained via inner product
x (t) = a cos(ω t) + b cos (2 ω t)
<x (t), cos(ω t) > = <a cos(ω t), cos(ω t) > + <b cos (2 ω t), cos(ω t) > = a (?)
If cos(ω t) and cos(2 ω t) are orthogonal

## Slide 20: Intuition of FT
Two dimension orthogonal basis
(a, b) = a (1,0) + b (0,1)
Functional space basis
x (t) = a cos(ω t) + b cos (2 ω t)

## Slide 21: Intuition of FT
It turns out that we can define the inner product
in the signal space

## Slide 22: Intuition of FT
Cos ( 2 p t)
Cos ( 2*2 p t)
Cos ( 2 p t) * Cos ( 2*2 p t)

## Slide 23: Intuition of FT
{ cos (n ω t ), n=1,2…} are orthogonal
they form orthogonal bases
Cos ( 2 p t)
Cos ( 2*2 p t)
Cos ( 2 p t) * Cos ( 2*2 p t)

## Slide 24: Intuition of FT
It turns out that we can define the inner product
in the signal space
In particular, we have
x (t) = a cos(ω t) + b cos (2 ω t)
a = <X(t), cos(ω t)> =
b = ?

## Slide 25: Intuition of FT
(1 0 0 0 0 0)
(0 1 0 0 0 0 )
(0 0 1 0 0 0)
(0 1 0 1 0 0)
(0 1 0 0 1 0)
(0 0 0 0 0 1)
X
X1
X2
X3
x4
X5
X6
In an n-dim Euclidean space, we decompose any vector X in terms of orthogonal bases
Coefficient is obtained by inner product between a basis and X
We sometime call xi weight
X = x1 (1 0 0 0 0 0) + x2(0 1 0 0 0 0 ) + … + x6 (0 0 0 0 0 1)

## Slide 26: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
A5
A6
……….

## Slide 27: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
A5
A6
……….
cos (2 ω t )

## Slide 28: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
A5
A6
……….
cos (2 ω t )
cos (3 ω t )

## Slide 29: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
A5
A6
……….
cos (2 ω t )
cos (3 ω t )
cos (4 ω t )

## Slide 30: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
0
A6
……….
cos (2 ω t )
cos (3 ω t )
cos (4 ω t )

## Slide 31: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
0
A6
cos (2 ω t )
cos (3 ω t )
cos (4 ω t )

## Slide 32: Intuition of FT
cos (ω t )
X(t)
A1
A2
A3
A4
0
A6
……….
cos (2 ω t )
cos (3 ω t )
cos (4 ω t )
In an n-dim Euclidean space, we decompose any vector X in terms of orthogonal bases
Coefficient is obtained by inner product between a basis and X
We sometime call xi weight

## Slide 33: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases

## Slide 34: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases

## Slide 35: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases
where A0 is the d.c. term, and T is the period of the waveform.

## Slide 36: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases
where A0 is the d.c. term, and T is the period of the waveform.

## Slide 37: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases
where A0 is the d.c. term, and T is the period of the waveform.

## Slide 38: FT: Fourier Thm in terms of Sin and Cos
simply a generalization of common knowledge of the Euclidean space
{ 1, cos (nωt), sin(nwt), n=1,2…} are orthogonal and complete
they form orthogonal bases
where A0 is the d.c. term, and T is the period of the waveform.

## Slide 39: Example I
x(t)=1, 0< t < p, 2p < t < 3p, 0 otherwise
Hence x(t) is a signal with a period of 2p
p 2p 3p 4p

## Slide 40: Example I
Finally, we have

## Slide 41
Frequency domain
Example I
The description of a signal in terms of its constituent frequencies is called its
frequency (power) spectrum.
2/p
|X(F)|

## Slide 42
Frequency domain
Example I
2/p
|X(F)|
Time domain
=

## Slide 43: Example I
A periodic signal is uniquely determined by its coefficients {An, Bn}.
If we truncated the series into finite term, the signal can be approximated by a finite sines as shown below (compression, MP3, MP4, JPG, … )
one term
Two terms
Three terms
Five terms

## Slide 44
Example II (understanding music)

## Slide 45: a. Pure tone: Script1_1.m
Example II
This confirms our earlier believe that it is a signal
with a finite bandwidth (N-S sampling Thm)

## Slide 46: Digital Music