## Slide 1: DCSP-6: Applications
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2: Recap
In general, a signal with T = 2p / w can be represented as follows
This is the idea of
JPEG, MP3, MP4
Compress

## Slide 3: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) ~ A0 + A1 cos(w t)

## Slide 4: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) ~ A0 + A1 cos(w t)+A2cos(2wt)

## Slide 5: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) ~ A0 + A1 cos(w t)+A2cos(2wt)+A3cos(3wt)

## Slide 6: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) ~ A0 + A1 cos(w t)+A2cos(2wt)+A3cos(3wt)
+ A4cos(4wt)+A5cos(5wt)+A6cos(6wt)
+ A7cos(7wt)+A8cos(8wt)+A9cos(9wt)

## Slide 7: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) = A0 + A1 cos(w t)+A2cos(2wt)+A3cos(3wt)
+ A4cos(4wt)+A5cos(5wt)+A6cos(6wt)
+ A7cos(7wt)+A8cos(8wt)+A9cos(9wt)
+ …

## Slide 8: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) = A0 + A1 cos(w t)+A2cos(2wt)+A3cos(3wt)
+ A4cos(4wt)+A5cos(5wt)+A6cos(6wt)
+ A7cos(7wt)+A8cos(8wt)+A9cos(9wt)
+ …
A1
A2
A3

## Slide 9: Recap
In general, a signal with T=2p/w can be represented as follows
T 2T
X(t) = A0 + A1 cos(w t)+A2cos(2wt)+A3cos(3wt)
+ A4cos(4wt)+A5cos(5wt)+A6cos(6wt)
+ A7cos(7wt)+A8cos(8wt)+A9cos(9wt)
+ …
A1
A2
A3
TIME
FREQUENCY

## Slide 10: Recap
In general, a signal with T=2p/w can be represented as follows
The more terms we have, the more accurate: compression
The plot of {An, Bn} against { n} is called frequency spectrum

## Slide 11: b. Different waveforms Script1_2.m
Example II
This confirms our earlier believe that it is a signal
without bandlimit (N-S sampling Thm)

## Slide 12: Bandwidth can be properly defined
Bandwidth is the difference between the upper and lower frequencies in a set of frequencies. It is typically measured in hertz

## Slide 13: Bandwidth can be properly defined
Bandwidth is the difference between the upper and lower frequencies in a continuous set of frequencies. It is typically measured in hertz
0 B Frequency
Power

## Slide 14: C. Approximation (compression) Script1_3.m
Example II
Without doing much, we can compress the original data now,
as in Example I.

## Slide 15: In detail

## Slide 16: Today’s Summary
General form of FT
A few applications (6 more precisely)
Noise

## Slide 17: FT: Neat Form; to remember easily
In general, a signal can be represented as follows

## Slide 18: FT: Neat Form
In general, a signal can be represented as follows
C-n
Cn

## Slide 19: FT : Neat Form
Which is the exponential form of the Fourier series.
In this expression the values Cn are complex number, we have
x(t) {Cn ,n=…,-1,0,1,2,…, }
FT
T 2T
TIME
FREQUENCY

## Slide 20: FT : Neat Form
Which is the exponential form of the Fourier series.
In this expression the values Cn are complex number, we have
x(t) {Cn ,n=…,-1,0,1,2,…, }
FT
IFT
where w = (2 p) / T

## Slide 21: FT in complex exponential
If the periodic signal is replace with an aperiodic signal (general case)
FT is given by
Is that deadly simple?

## Slide 22: Example I
Consider the case of a rectangular pulse. In particular, let us define
Its FT is given by
Which is called the Sinc function.

## Slide 23
Example I
There are a number of features to note:
The bandwidth of the signal is only approximately finite.
Most of the energy is contained in a limited regions
called the main-lobe.
However, some energy is found at all frequencies.
The spectrum has positive and negative
frequencies.
These are symmetric about the origin.
This may seem non-intuitive, but can be seen
from equations in periodic case
Note that the spectrum is continuous now:
X(F)= Sinc function
power
Frequency

## Slide 24: Fourier's Song

## Slide 25: The world has changed
Frequency eye
This module and a few following ones will make use of the frequency information

## Slide 26: This module is about practical applications
How to use this idea?

## Slide 27
1 10
Frequency domain
Time domain
S1(t)= 10 cos(2pt) + cos(10*2pt)
for i=1:10000
x(i)=10*cos(i*0.01)+cos(i*10*0.01);
End
Sound(x)
App I

## Slide 28
Frequency domain
Time domain
S2(t)= cos(2pt) + 10 cos(10*2pt)
for i=1:10000
x(i)=1*cos(i*0.01)+10*cos(i*10*0.01);
End
Sound(s)
App I

## Slide 29
In frequency domain, the height of the spectrum indicates the energy of the corresponding signal.
For example,
for S1, energy concentrating on the signal cos(2pt),
a low frequency signal
for S2, energy concentrating on the signal cos(10*2pt),
a high frequency signal
App I

## Slide 30: App II: Touch-tone dialing

## Slide 31: App II: Touch-tone dialing
Freqs 1209 Hz 1336 Hz 1477 Hz 1633 Hz
697 Hz 1 2 3 A
770 Hz 4 5 6 B
852 Hz 7 8 9 C
941 Hz * 0 # D
touch_tone.m
(1)=An1 cos(n1 w0t) +An2cos(n2w0t)
1 Hz = w0
Your phone is a section (two terms)
of a FT

## Slide 32
In bluetooth, for example, to improve resistance to radio frequency interference by avoiding using crowded frequencies in the hopping sequence.
In military use, it is a simple idea (radio guided torpedo, for example)
APP III: Spread spectrum techniques

## Slide 33: App IV: instruments
We all know about pitch…
It is really about frequency, or cycles per seconds
How about harmonics?
This is what gives the timbre of an instrument!

## Slide 34: App IV: instruments
The played note is the frequency of
the first peak: 220Hz (note A) in this case
Other peaks are called harmonics:
they define the typical sound of
the instrument
Without Fourier, we could have
been lost
When you play an instrument,
It is a section of a FT

## Slide 35: App V: MP3+MP4
How can an MP3 song sound so well,
while being so compressed?
Compression in a sense introduces noise.
a combination of our hearing system + FT

## Slide 36: App V: MP3+MP4
>> r = audiorecorder(22050, 16, 1);
>> record(r)
>> stop(r)
>> mySpeech = getaudiodata(r, 'int16'); % get data as int16 array
>> audiowrite('compress_3.wav',mySpeech,Fs);
load handel.mat
filename = 'handel.wav';
audiowrite(filename,y,Fs);
clear y Fs
Original noiseless music
Original musie + noise 2  SNR =13 dB
Same amount of noise
Impressive difference of sound
What is the secret?

## Slide 37
App V: MP3+MP4

## Slide 38
App V: MP3+MP4
MP3: complex compression algorithm that introduces errors
MP3 minimizes the perceived quality decay by shaping the compression errors

## Slide 39: App VI: Mind Reading
MRI is a medical imaging technique
to visualize your internal body
structure and/or activity in detail
Using a physics term: it measures the
oscillations of hydrogen nuclei when
stimulated by different radio-frequency
magnetic fields
Reading you mind with FT
My
brain
activity
during
one
scan

## Slide 40: App VI: Mind Reading
MRI is a medical imaging technique
to visualize your internal body
structure and/or activity in detail
Using a physics term: it measures the
oscillations of hydrogen nuclei when
stimulated by different radio-frequency
magnetic fields
Reading you mind with FT
My
brain
activity
during
one
scan
It is not about
sex

## Slide 41: App VI: Mind Reading
Using a DCSP term: it measures the FT of the internal structure
and/or activity of interest
How does the collected data looks like?
img=(T1_Image(:,:,50));
img = fftshift(img(:,:));
F = fft2(img);
figure;
imagesc(100*log(1+abs(fftshift(F)))); colormap(gray);
title('magnitude spectrum');
figure;
imagesc(angle(F)); colormap(gray);
title('phase spectrum');

## Slide 42
Little information about the subject can be gathered in the original picture
An inverse Fourier transform of the data reveals the slice of a human head activity
App VI: Mind Reading

## Slide 43
App VI: Mind Reading
Human Brain Project was one of the two projects with a budge of 1B Euros for ten years each
(another is graphene) in 2013
The main purpose is to simulate the Brain
=
USA matched with a 4.5 B US Dollars in 2014
China will do as well

## Slide 44
App VI: Mind Reading
Spinnaker can simulate 1% of our human brain cells (Steve Furber 21st Jan 2020)

## Slide 45
von Neumann
Brain inspired AI (digital)