## Slide 1: DCSP-8: Signal Representation
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2: Correlation or covariance
Cov(X,Y) = E(X-EX)(Y-EY)
correlation coefficient is normalized covariance
Coef(X,Y) = E(X-EX)(Y-EY) / [s(X)s(Y)]
Positive correlation, Negative correlation
No correlation (independent)

## Slide 3: Stochastic process = signal
A stochastic process is a collection of random variables x[n], for each fixed [n], it is a random variable
Signal is a typical stochastic process
To understand how x[n] evolves with n, we will look at auto-correlation function (ACF)
ACF is the correlation between k steps

## Slide 4: Stochastic process
>> clear all
close all
n=200;
for i=1:10
x(i)=randn(1,1);
y(i)=x(i);
end
for i=1:n-10
y(i+10)=randn(1,1);
x(i+10)=.8*x(i)+y(i+10);
end
plot(xcorr(x)/max(xcorr(x)));
hold on
plot(xcorr(y)/max(xcorr(y)),'r')
two signals are generated: y (red) is simply randn(1,200)
x (blue) is generated x[i+10]=.8*x[i] + y[i+10]
For y, we have g(0)=1, g(n)=0, if n is not 0 : having no memory
For x, we have g (0)=1, and g (n) is not zero, for some n: having memory

## Slide 5: white noise w[n]
White noise is a random process we can not predict at all (independent of history)
In other words, it is the most ‘violent’ noise
White noise draws its name from white light which will become
clear in the next few lectures

## Slide 6
The most ‘noisy’ noise is a white noise since its autocorrelation is zero, i.e.
corr(w[n], w[m])=0 when
Otherwise, we called it colour noise since we can predict some outcome of w[n], given w[m], m<n
white noise w[n]

## Slide 7: DCSP-8: Signal Representation
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 8
long-term memory
short-term memory
Restoring Memory
MIMO Biomimetic device mimics signal processing function of hippocampal neural circuits
Interface with the hippocampus using multi-electrode arrays
Transform upstream hippocampal signals into downstream hippocampal signals using a computational model
By-pass damaged hippocampal region
Restore episodic memory functions

## Slide 9
long-term memory
short-term memory
Restoring Memory
Memories

## Slide 10
NeuralLink (Elon Musk)

## Slide 11: Spectrogram: real life example

## Slide 12: Sequences and their representation
A sequence is an infinite series of real numbers { x[n] }
{ x[n] } = {…, x[-1], x[0], x[1], x[2], … , x[n], … }
Represent a sampled signal, i.e. x[n] = x(nT),
where x(t) is continuous function of time

## Slide 13: Sequences and their representation
A sequence is an infinite series of real numbers { x[n] }
{ x[n] } = {…, x[-1], x[0], x[1], x[2], … , x[n], … }

## Slide 14: Discrete Time Fourier Transform (DTFT)
The basic tool of signal analysis is
the Fourier transform or DTFT

## Slide 15: Definition and properties:
DTFT gives the frequency representation of a discrete time sequence with infinite length.

## Slide 16: Definition and properties:
DTFT gives the frequency representation of a discrete time sequence with infinite length.
Define ( w = 2pF)
Note that X(w) has a period of 2p

## Slide 17: Definition and properties:
p 2p
p 2p
Visualize X(w)
Plot it in the magnitude and phase plane

## Slide 18
The DTFT gives the frequency representation of a discrete time sequence with infinite length.
X(w): frequency domain
x [n]: time domain
Definition and properties:

## Slide 19: Example I
the unit impulse
Consider the delta (impulse) function x[n]=d[n], we have
x[n]=d[n],

## Slide 20: Example I
the unit impulse
Consider the delta (impulse) function x[n]=d[n], we have
amplitude
phase
-p p
-p p

## Slide 21: Example I
the unit impulse
Consider the delta (impulse) function x[n]=d[n], we have
amplitude
phase
-p p
-p p

## Slide 22: Example II
Consider the signal
x[n]=0.5n, n=0,1,2,…
Then

## Slide 23: Example II
Consider the signal
x[n]=0.5n, n=0,1,2,…
Then

## Slide 24: Example II
Consider the signal
x[n] = 0.5n, n = 0,1,2,…
Then

## Slide 25
Example II
h=0.01;
N=4000;
for i=1:N
t(i)=(i-N/2)*h;
x(i)=1/(1-0.5*exp(-j*t(i)));
end
figure(1)
plot(t,abs(x));
figure(2)
plot(t,phase(x));

## Slide 26: Computation of the DTFT
Fourier approach to signal analysis is based on
the expansion of a signal in terms of sinusoids
or, more precisely, complex exponentials.
Analyzing a signal by determining the
frequencies contributing to its spectrum in terms
of magnitudes and phases.

## Slide 27: Computation of the DTFT
In practice, we do not have infinite memory, we
do not have infinite time, and signal does not
have infinite duration.
In addition, the spectrum of the signal changes
with time, just as music is composed of different
notes that change with time.

## Slide 28: Computation of the DTFT
Consequently, the DTFT generally is not
computable unless we have an analytical
expression for the signal we analyze, in which
case we can compute it symbolically.

## Slide 29
But most of the time this is not the case,
especially when we want to determine the
frequency spectrum of a signal measured from
an experiment.
In this situation, develop an algorithm that can
be computed numerically in a finite number of
steps, such as the discrete Fourier transform
(DFT), a special case of DTFT.
Computation of the DTFT

## Slide 30
For a given data set
{x[1], …x[N]},
it is equivalent to
{…,0, x[1], …, x[N], 0, 0,…}.
Using DTFT, we have
DFT and DTFT

## Slide 31
It turns out that we can sample it (computable with computer),
at w = 2p k / N, k = 0,1,…,N-1
DFT and DTFT

## Slide 32: DFT
Definition: The discrete Fourier transform (DFT) and its own
inverse DFT (IDFT) associated with a vector
X = ( X[0], X[1], … , X[N-1] )
to a vector
x = ( x[0], x[1], …, x[N-1] )
of N data points, is given by

## Slide 33: Example I
Consider the delta (impulse) function x[n]=d[n], we have
amplitude
phase
0 2p
0 2p

## Slide 34: Example I
sample it (computable with computer), at w = 2p k / N, k = 0,1,…,N-1
amplitude
phase
0 2p
0 2p

## Slide 35: Example I
sample it (computable with computer), at w = 2p k / N, k = 0,1,…,N-1
amplitude
phase
0 2p
0 2p
For example, we have N = 4
2p 0/N= 0
2p 1/N = p/2
2p 2/N = p
2p 3/N = 3p/4

## Slide 36: Example I
sample it (computable with computer), at w = 2p k / N, k = 0,1,…,N-1
For example, we have N = 4
2p 0/N= 0
2p 1/N = p/2
2p 2/N = p
2p 3/N = 3p/4
(X [0] X[1] X[2] X[3] ) = (1 1 1 1) = DTFT((x[0] x[1] x[2] x[3])) = DFT((1 0 0 0))
amplitude
phase
0 2p
0 2p

## Slide 37: DFT I (Essential facts)
Remembering that the data is
x[0], x[1], …, x[N-1]
We have N (complex plane ) points in the frequency domain
X[0], X[1], …, X[N-1]
k=0

## Slide 38: DFT I (Essential facts)
Remembering that the data is
x[0], x[1], …, x[N-1]
We have N (complex plane ) points in the frequency domain
X[0], X[1], …, X[N-1]
k=0
k=1

## Slide 39: DFT I (Essential facts)
Remembering that the data is
x[0], x[1], …, x[N-1]
We have N (complex plane ) points in the frequency domain
X[0], X[1], …, X[N-1]
k=0
k=1
k=2

## Slide 40: DFT I (Essential facts)
Rewritten it in matrix form, assume the data is x[0], x[1], …, x[N-1]

## Slide 41: DFT I (Essential facts)
Rewritten it in matrix form, assume the data is x[0], x[1], …, x[N-1]
DATA
DFT