## Slide 1: DCSP-10: Applications
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2: Applications
Power spectrum estimate
Image
Sampling theorem

## Slide 3
X’ = A x’

## Slide 4
Issues on noise
Two sets of random noise (100 points each, upper panel)
Power Spectrum (bottom panel)
Make sense?

## Slide 5
Issues on noise
When N is large
abs (DFT ( {x[n], n=0, …, N-1} ) )  DFT ( {g [n] } )
where g [n] is the auto-correlation function (ACF)
Remember that the ACF of white noise is

## Slide 6
Issues on noise
Remember that the ACF of white noise is
Powers are equally distributed at each frequency
Hence the name of ‘white noise’
Colour noise: not equally distributed (ACF is not delta)

## Slide 7
Issues on noise
Remember that the ACF of white noise is
Powers are equally distributed at each frequency
Hence the name of ‘white noise’
Colour noise: not equally distributed (ACF is not delta)
White light passes a prism
White light goes through a prism

## Slide 8: Spectrogram: real life example

## Slide 9: Math
1
T
T
WT[n]
You can certainly choose many ‘windows’ here: triangle, Gaussian, Hamming etc.
1
1 T+1
WT[n-1]
1
m+1 T+m
WT[n-m]

## Slide 10: Matlab
A few words on Matlab
periodogram pwelch
It is essentially fft
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
It is slightly advanced

## Slide 11: Matlab
A few words on Matlab
periodogram pwelch
It is essentially fft
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
It is slightly advanced
Abs(fft(x))

## Slide 12: Matlab
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
It is slightly advanced
Abs(fft(x))
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
In Welch, essentially the signals are divided into many segments
For each segments, an FFT is carried
The summation of FFT is plotted and hence the noise is averaged out
A few words on Matlab
periodogram pwelch
It is essentially fft

## Slide 13: Understanding the plot
Sampling rate is Fs, the largest (fastest) frequency from the data is then Fs/2
Remembering that our frequency domain is in [0 2p] which matches to [0 Fs]
Divide [0 Fs] into N intervals and plot abs X[k] against kFs/N which gives power against frequency
Since it is symmetric, we sometime only plot out [0, Fs//2]
Here Fs =1 0 Hz

## Slide 14: Spectrogram
It is called STFT (short time Fourier transform)
The obtained results are plotted using colour map as in the next figure: spectrogram

## Slide 15: Math
1
T
T
WT[n]
You can certainly choose many ‘windows’ here: triangle, Gaussian, Hamming etc.

## Slide 16: Matlab
A few words on Matlab
periodogram pwelch
It is essentially fft
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
It is slightly advanced

## Slide 17: Matlab
A few words on Matlab
periodogram pwelch
It is essentially fft
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
It is slightly advanced
Abs(fft(x))

## Slide 18: Matlab
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
It is slightly advanced
Abs(fft(x))
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
In Welch, essentially the signals are divided into many segments
For each segments, an FFT is carried
The summation of FFT is plotted and hence the noise is averaged out
A few words on Matlab
periodogram pwelch
It is essentially fft

## Slide 19: Spectrogram
In real life examples, all signals change with time (music for example)

## Slide 20: Spectrogram
In real life example, all signals change with time (music for example)
Using sliding window to sample signals and calculate PSD

## Slide 21: Spectrogram
In real life example, all signals change with time (music for example)
Using sliding window to sample signals and calculate PSD

## Slide 22: Spectrogram
In real life example, all signals change with time (music for example)
Using sliding windows to sample signals and calculate PSD

## Slide 23: Spectrogram
Time (sec)
Frequency
1 Hz
3 Hz

## Slide 24: Example I
t=0:0.001:2; % 2 secs @ 1kHz sample rate
y=chirp(t,100,1,200,'q'); % Start @ 100Hz, cross 200Hz at t=1sec
spectrogram(y,128,120,128,1E3); % Display the spectrogram
title('Quadratic Chirp: start at 100Hz and cross 200Hz at t=1sec');
sound(y)
y=chirp(t,100,1,200,'q'); % Start @
Fs=5000;
filename = 'h.wav';
audiowrite(filename,y,Fs);
Time (sec)
Frequency

## Slide 25: Example II
);
sound(y)
t=0:0.001:20; % 2 secs @ 1kHz sample rate
y=chirp(t,100,1,200,'q'); % Start @ 100Hz, cross 200Hz at t=1sec
spectrogram(y,128,120,128,1E3); % Display the spectrogram
title('Quadratic Chirp: start at 100Hz and cross 200Hz at t=1sec');
Fs=6000;
filename='h.wav';
audiowrite(filename,y,Fs);
Time (sec)
Frequency

## Slide 26: A Matlab Example
close all
clear all
load handel;
figure(1)
plot(y);
xlabel('time')
T=size(y);
for i=1:T(1,1)
fre_x(i)=i*Fs/T(1,1);
end
figure(2)
plot(fre_x, abs(fft(y)))
xlabel('Hz')
figure(3)
spectrogram(y,128,120,[],Fs);
T1=floor(T(1,1)/2);
omega1=1000;
for i=1:T(1,1)-T1;
z(i,1)=y(i,1)+.3*cos(2*pi*omega1*i/Fs);
end
omega2=2000;
for i=T-T1+1:T(1,1);
z(i,1)=y(i,1)+.3*cos(2*pi*omega2*i/Fs);
end
figure(5)
plot(z);
xlabel('time')
figure(6)
plot(fre_x,abs(fft(z)))
xlabel('Hz')
figure(7)
spectrogram(z,128,120,[],Fs);
for i=1:T(1,1);
zn(i,1)=y(i,1)+.3*randn(1,1);
end
figure(8)
plot(zn);
xlabel('time')
figure(9)
plot(fre_x,abs(fft(zn)))
xlabel('Hz')
figure(10)
spectrogram(zn,128,120,[],Fs);
;
Three signals

## Slide 27: A Matlab Example
close all
clear all
load handel;
figure(1)
plot(y);
xlabel('time')
T=size(y);
for i=1:T(1,1)
fre_x(i)=i*Fs/T(1,1);
end
figure(2)
plot(fre_x, abs(fft(y)))
xlabel('Hz')
figure(3)
spectrogram(y,128,120,[],Fs);
T1=floor(T(1,1)/2);
omega1=1000;
for i=1:T(1,1)-T1;
z(i,1)=y(i,1)+.3*cos(2*pi*omega1*i/Fs);
end
omega2=2000;
for i=T-T1+1:T(1,1);
z(i,1)=y(i,1)+.3*cos(2*pi*omega2*i/Fs);
end
figure(5)
plot(z);
xlabel('time')
figure(6)
plot(fre_x,abs(fft(z)))
xlabel('Hz')
figure(7)
spectrogram(z,128,120,[],Fs);
for i=1:T(1,1);
zn(i,1)=y(i,1)+.3*randn(1,1);
end
figure(8)
plot(zn);
xlabel('time')
figure(9)
plot(fre_x,abs(fft(zn)))
xlabel('Hz')
figure(10)
spectrogram(zn,128,120,[],Fs);
;
Original signal
+ disturbance
+ noise

## Slide 28: A Matlab Example
close all
clear all
load handel;
figure(1)
plot(y);
xlabel('time')
T=size(y);
for i=1:T(1,1)
fre_x(i)=i*Fs/T(1,1);
end
figure(2)
plot(fre_x, abs(fft(y)))
xlabel('Hz')
figure(3)
spectrogram(y,128,120,[],Fs);
T1=floor(T(1,1)/2);
omega1=1000;
for i=1:T(1,1)-T1;
z(i,1)=y(i,1)+.3*cos(2*pi*omega1*i/Fs);
end
omega2=2000;
for i=T-T1+1:T(1,1);
z(i,1)=y(i,1)+.3*cos(2*pi*omega2*i/Fs);
end
figure(5)
plot(z);
xlabel('time')
figure(6)
plot(fre_x,abs(fft(z)))
xlabel('Hz')
figure(7)
spectrogram(z,128,120,[],Fs);
for i=1:T(1,1);
zn(i,1)=y(i,1)+.3*randn(1,1);
end
figure(8)
plot(zn);
xlabel('time')
figure(9)
plot(fre_x,abs(fft(zn)))
xlabel('Hz')
figure(10)
spectrogram(zn,128,120,[],Fs);
;
Abs(fft) vs Frequency

## Slide 29: A Matlab Example
close all
clear all
load handel;
figure(1)
plot(y);
xlabel('time')
T=size(y);
for i=1:T(1,1)
fre_x(i)=i*Fs/T(1,1);
end
figure(2)
plot(fre_x, abs(fft(y)))
xlabel('Hz')
figure(3)
spectrogram(y,128,120,[],Fs);
T1=floor(T(1,1)/2);
omega1=1000;
for i=1:T(1,1)-T1;
z(i,1)=y(i,1)+.3*cos(2*pi*omega1*i/Fs);
end
omega2=2000;
for i=T-T1+1:T(1,1);
z(i,1)=y(i,1)+.3*cos(2*pi*omega2*i/Fs);
end
figure(5)
plot(z);
xlabel('time')
figure(6)
plot(fre_x,abs(fft(z)))
xlabel('Hz')
figure(7)
spectrogram(z,128,120,[],Fs);
for i=1:T(1,1);
zn(i,1)=y(i,1)+.3*randn(1,1);
end
figure(8)
plot(zn);
xlabel('time')
figure(9)
plot(fre_x,abs(fft(zn)))
xlabel('Hz')
figure(10)
spectrogram(zn,128,120,[],Fs);
;

## Slide 30: A Matlab Example
close all
clear all
load handel;
figure(1)
plot(y);
xlabel('time')
T=size(y);
for i=1:T(1,1)
fre_x(i)=i*Fs/T(1,1);
end
figure(2)
plot(fre_x, abs(fft(y)))
xlabel('Hz')
figure(3)
spectrogram(y,128,120,[],Fs);
T1=floor(T(1,1)/2);
omega1=1000;
for i=1:T(1,1)-T1;
z(i,1)=y(i,1)+.3*cos(2*pi*omega1*i/Fs);
end
omega2=2000;
for i=T-T1+1:T(1,1);
z(i,1)=y(i,1)+.3*cos(2*pi*omega2*i/Fs);
end
figure(5)
plot(z);
xlabel('time')
figure(6)
plot(fre_x,abs(fft(z)))
xlabel('Hz')
figure(7)
spectrogram(z,128,120,[],Fs);
for i=1:T(1,1);
zn(i,1)=y(i,1)+.3*randn(1,1);
end
figure(8)
plot(zn);
xlabel('time')
figure(9)
plot(fre_x,abs(fft(zn)))
xlabel('Hz')
figure(10)
spectrogram(zn,128,120,[],Fs);
;

## Slide 31
Will come back to it in the next few weeks
after we learn how to design filters
A Matlab Example

## Slide 32: Image Processing
two-dimensional signal x[n1,n2], n1,n2∈Z
indices locate a point on a grid → pixel
grid is usually regularly spaced
values x[n1,n2] refer to the pixel’s appearance

## Slide 33
Gray scale images: scalar pixel values
color images: multidimensional pixel values in a color space (RGB for example)
we can consider the single components separately:
Image Processing

## Slide 34: DFT for image
DFT for x
IDFT for X
X = A N1 x N1 x N1 x N2 B N2 x N2

## Slide 35
2 | 

## Slide 36: clear all close all figure(1) I = imread('peppers.png'); imshow(I); K=rgb2gray(I); figure(2) F = fft2(K); figure; imagesc(100*log(1+abs(fftshift(F)))); colormap(gray); title('magnitude spectrum'); figure; imagesc(angle(F)); colormap(gray)
Original picture Gray scale picture
Example I

## Slide 37: Example I

## Slide 38: Example I
All low frequency information is here
FF=(100*log(1+abs(fftshift(F))));
for i=1:384
for j=1:512
ss=sqrt((i-192)*(i-192)+(j-256)*(j-256));
if(ss>100)
FF(i,j)=0;
end
end
end
figure; imagesc(FF); colormap(gray);
title('magnitude spectrum'); figure; imagesc(angle(FF)); colormap(gray)

## Slide 39: Example I
All low frequency information is here
FF=(100*log(1+abs(fftshift(F))));
for i=1:384
for j=1:512
ss=sqrt((i-192)*(i-192)+(j-256)*(j-256));
if(ss>100)
FF(i,j)=0;
end
end
end
figure; imagesc(FF); colormap(gray);
title('magnitude spectrum'); figure; imagesc(angle(FF)); colormap(gray)

## Slide 40: Example I
All high frequency information is here
FF=(100*log(1+abs(fftshift(F))));
for i=1:384
for j=1:512
ss=sqrt((i-192)*(i-192)+(j-256)*(j-256));
if(ss>100)
FF(i,j)=0;
end
end
end
figure; imagesc(FF); colormap(gray);
title('magnitude spectrum'); figure; imagesc(angle(FF)); colormap(gray)
?

## Slide 41: Image processing
Example II

## Slide 42
Example III: mind reading
IDFT2

## Slide 43: Sampling and reconstruction
The question we consider here is under
what conditions we can completely
reconstruct the original signal
x(t)
from its discretely sampled signal
x[n].

## Slide 44
Sampling and reconstruction
Theorem (Nyquist-Shannon sampling thm)
Exact reconstruction of a continuous-time signal from its samples is possible
if the signal is bandlimited and the sampling frequency is greater than twice
the signal bandwidth
Proof. The proof is again an application of FT, but we will not go through it here
Please read around. It is based upon the sinc function.

## Slide 45
At the end of the day, FT for signal x is only fft(x)
it is deadly easy
Hopefully and I am sure it will be useful for your
future career
Summary of FT

## Slide 46
At the end of the day, FT for signal x is only fft(x)
it is deadly easy
Hopefully it will be useful for your future career
I am proud of this
Summary of FT

## Slide 47: Remaining Issues?
Will you try to use FT to approximate them?

## Slide 48: Wavelet approach: 1980’s
Will you try to use FT to approximate them?
Wavelet

## Slide 49
Recap

## Slide 50: Wavelet: intuition

## Slide 51: Orthogonal bases

## Slide 52
S[n]=(56 40 8 24 48 48 40 16)’
S= 35h0-3h1+16 h2+10 h3+8 h4 – 8h5+ 0 h6 +12 h7
Where h is the Haar wavelet
h0= (1 1 1 1 1 1 1 1)’, h1=(1 1 1 1 -1 -1 -1 -1)’
……..
One example