## Slide 1: DCSP-9: DFT and PSD
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2
For a given data set
{x[1], …x[N]},
it is equivalent to
{…,0, x[1], …, x[N], 0, 0,…}.
Using DTFT, we have
DFT and DTFT

## Slide 3
It turns out that we can sample it (computable with computer),
at w = 2p k / N, k = 0,1,…,N-1
DFT and DTFT

## Slide 4: DFT
Definition: The discrete Fourier transform (DFT) and its own
inverse DFT (IDFT) associated with a vector
X = ( X[0], X[1], … , X[N-1] )
to a vector
x = ( x[0], x[1], …, x[N-1] )
of N data points, is given by

## Slide 5: Example I
Consider the delta (impulse) function x[n]=d[n], we have
amplitude
phase
0 2p
0 2p

## Slide 6: Example I
sample it (computable with computer), at w = 2p k / N, k = 0,1,…,N-1
amplitude
phase
0 2p
0 2p

## Slide 7: Example I
sample it (computable with computer), at w = 2p k / N, k = 0,1,…,N-1
amplitude
phase
0 2p
0 2p
For example, we have N = 4
2p 0/N= 0
2p 1/N = p/2
2p 2/N = p
2p 3/N = 3p/4

## Slide 8: Example I
sample it (computable with computer), at w = 2p k / N, k = 0,1,…,N-1
For example, we have N = 4
2p 0/N= 0
2p 1/N = p/2
2p 2/N = p
2p 3/N = 3p/4
(X [0] X[1] X[2] X[3] ) = (1 1 1 1) = DTFT((x[0] x[1] x[2] x[3])) = DFT((1 0 0 0))
amplitude
phase
0 2p
0 2p

## Slide 9: DFT I (Essential facts)
Remembering that the data is
x[0], x[1], …, x[N-1]
We have N (complex plane ) points in the frequency domain
X[0], X[1], …, X[N-1]
k=0

## Slide 10: DFT I (Essential facts)
Remembering that the data is
x[0], x[1], …, x[N-1]
We have N (complex plane ) points in the frequency domain
X[0], X[1], …, X[N-1]
k=0
k=1

## Slide 11: DFT I (Essential facts)
Remembering that the data is
x[0], x[1], …, x[N-1]
We have N (complex plane ) points in the frequency domain
X[0], X[1], …, X[N-1]
k=0
k=1
k=2

## Slide 12: DFT I (Essential facts)
Rewritten it in matrix form, assume the data is x[0], x[1], …, x[N-1]
A

## Slide 13: DFT I (Essential facts)
Rewritten it in matrix form, assume the data is x[0], x[1], …, x[N-1]
DATA
DFT

## Slide 14: DFT II
A*

## Slide 15: DFT II

## Slide 16: DFT II

## Slide 17: DFT III
Definition: The discrete Fourier transform (DFT) and its own
inverse DFT (IDFT) associated with a vector
X = ( X[0], X[1], … , X[N-1] )
to a vector
x = ( x[0], x[1], …, x[N-1] )
of N data points, is given by

## Slide 18: Modern version: graphic representation
x[0]
x[1]
x[N-2]
x[N-1]
X[0]
X[1]
X[N-2]
X[N-1]
1
1
1
1

## Slide 19
x[0]
x[1]
x[N-2]
x[N-1]
X[0]
X[1]
X[N-2]
X[N-1]
1
Exp(-j2pi/N)
Exp(-j2pi (N-2)/N)
Exp(-j2pi (N-1)/N)
Modern version: graphic representation

## Slide 20
x[0]
x[1]
x[N-2]
x[N-1]
X[0]
X[1]
X[N-2]
X[N-1]
1
Exp(-j2pi(N-2)/N)
Exp(-j2pi (N-2)(N-2)/N)
Exp(-j2pi (N-1)(N-2)/N)
Modern version: graphic representation

## Slide 21
x[0]
x[1]
x[N-2]
x[N-1]
X[0]
X[1]
X[N-2]
X[N-1]
1
Exp(-j2pi(N-1)/N)
Exp(-j2pi (N-2)(N-1)/N)
Exp(-j2pi (N-1)(N-1)/N)
Modern version: graphic representation

## Slide 22
x[0]
x[1]
x[N-2]
x[N-1]
X[0]
X[1]
X[N-2]
X[N-1]
A:weight matrix
x[0]
x[1]
x[N-2]
x[N-1]
A*/N:weight matrix
Modern version: graphic representation

## Slide 23: Modern version: Neural Networks
x[0]
x[1]
x[N-2]
x[N-1]
f(x[0])
f(x[1])
f(X[M-1])
W:weight matrix
The only difference is that the output is f(x[k]) and W could be any matrix

## Slide 24: Modern version: Neural Networks
x[0]
x[1]
x[N-2]
x[N-1]
W:weight matrix
f(x[0])
f(x[1])
f(X[M-1])
The only difference is that the output is f(x[k]) and W could be any matrix
f(x[0])
f(x[1])
f(X[M-1])
f(x[0])
f(x[1])
f(X[M-1])

## Slide 25: Summary
DFT and IDFT are simple: multiplication of matrices !!!!

## Slide 26: Summary
DFT and IDFT are simple: multiplication of matrices !!!!
DFT( Data) enables us to view the data in the frequency domain
IDFT can uniquely enables us to recover the data from its frequency domain (MRI machine)

## Slide 27: Example
Let (x[0], x[1], x[2], x[3]) = (1 2 -1 -1) be a data vector
of length N=4. Work out its DFT (X[0], X[1], X[2], X[3])

## Slide 28: Example
Let (x[0], x[1], x[2], x[3]) = (1 2 -1 -1) be a data vector
of length N=4. Work out its DFT (X[0], X[1], X[2], X[3])

## Slide 29: Example
[1 2 -1 -1]
Time domain
2+3j
2-3j
[ 1 2+3 j -1 2-3 j ]
Complex plane
a
-a
x [n]
X [ k ]

## Slide 30: Example
Time domain
2+3j
2-3j
Complex plane
a
-a
x [n]
X [ k ]

## Slide 31: Example
Time domain
Complex plane (polar coordinate)
Frequency domain
a
Amplitude
phase
x [n]
1
-a

## Slide 32: Matlab demo
x=[1 2 -1 -1];
X=fft(x)
X =
1.0000 + 0.0000i 2.0000 - 3.0000i -1.0000 + 0.0000i 2.0000 + 3.0000i
ifft(X)
ans =
1 2 -1 -1

## Slide 33: Recap
FT [ integral (x*exp) ]
DTFT [ sum (x*exp) ]
DFT [multiplication of two matrices]
Discretion
Truncation

## Slide 34: FFT: Fast Fourier Transform
DFT is the basis of a number of applications.
One of the most important tools in digital signal processing.
The problem is that a brute-force implementation would hardly be feasible in real time (even for a data set of modest length).

## Slide 35: FFT: Fast Fourier Transform
DFT can be computed in a very efficient way, exploiting the very structure of the algorithm.
For a data set of length N, the complexity of the
FFT grows as N log N
DFT computed by brute force grow as N2.
FFT is widely used in many applications.

## Slide 36: Fourier

## Slide 37: Applications
cover some today and tomorrow
Essentially, the remaining of the module is its applications
Frequency eye

## Slide 38: I. DFT for spectral estimation
One of the uses is to estimate the frequency spectrum of a signal.
The Fourier transform produces a spectrum from which the original
function can be reconstructed by an inverse transform.
In order to do that, it preserves not only the magnitude of each frequency component, but also its phase.
Represented as a 2-dimensional vector or a complex number, or as magnitude and phase (polar coordinates).
In graphical representations, often only the magnitude (or squared magnitude) component is shown.
Referred to as a power spectrum Density (PSD)

## Slide 39
close all
N=10; %sampling rate N Hz
T=10; % time
d1=1; % first period
d2=3 % second period
for i=1:T*N
t(i)=i/N;
x(i)=cos(d1*2*pi*i/N)+cos(d2*2*pi*i/N);
end
figure(1)
plot(t,x)
figure(2)
plot(t*N/(T),abs(fft(x)))
xlim([0 N/2]);
xlabel('Hz')
Locating tones
Time domain (sec)
Frequency domain (amplitude only)

## Slide 40
clear all
close all
sampling_rate=100;%Hz
omega=30; %signal frequecy Hz
N=20000; %total number of samples
for i=1:N
x_sound(i)=cos(2*pi*omega*i/sampling_rate); %signal
x(i)=x_sound(i)+2*randn(1,1); %signal+noise
axis(i)=sampling_rate*i/N; % for psd
time(i)=i/sampling_rate; % for time trace
end
subplot(1,2,1)
plot(time,x); %signal + noise, time trace
xlabel('second')
ylabel('x')
subplot(1,2,2)
plot(axis,abs(fft(x)),'r'); % magnitude of signal
xlabel('Hz');
ylabel('Amplitude')
sound(x_sound)
Mysterious sound
Simple Matlab program is left on slides
Fig. 2

## Slide 41
clear all
close all
sampling_rate=100;%Hz
omega=30; %signal frequecy Hz
N=20000; %total number of samples
for i=1:N
x_sound(i)=cos(2*pi*omega*i/sampling_rate); %signal
x(i)=x_sound(i)+2*randn(1,1); %signal+noise
axis(i)=sampling_rate*i/N; % for psd
time(i)=i/sampling_rate; % for time trace
end
subplot(1,2,1)
plot(time,x); %signal + noise, time trace
xlabel('second')
ylabel('x')
subplot(1,2,2)
plot(axis,abs(fft(x)),'r'); % magnitude of signal
xlabel('Hz');
ylabel('Amplitude')
sound(x_sound)
Mysterious sound
Simple Matlab program is left on slides
Fig. 2

## Slide 42
Mysterious sound: sampling window
Note the magnitude of the y-axis
Fig. 2

## Slide 43
Mysterious sound: sampling window
Note the magnitude of the y-axis

## Slide 44
Issues on Signals
FFT
Use this signal
{x[0], …, x[N-1]}

## Slide 45
Issues on Signals
FFT
Use this signal
Use this signal
FFT
{x[0], …, x[N-1]}
{x[0], …, x[2N-1]}

## Slide 46
Issues on Signals
FFT
Use this signal
Use this signal
FFT
{x[0], …, x[3N-1]}
{x[0], …, x[8N-1]}

## Slide 47
Issues on Signals
FFT
Use this signal
Use this signal
FFT
With the increased
signal length
The power increases
We can locate the signal more precisely

## Slide 48
Issues on noise
When N is large
abs (DFT ( {x[n], n=0, …, N-1} ) )  DFT ( {g [n] } )
where g [n] is the auto-correlation function (ACF)
Remember that the ACF of white noise is

## Slide 49
Issues on noise
When N is large
abs (DFT ( {x[n], n=0, …, N-1} ) )  DFT ( {g [n] } )
where g [n] is the auto-correlation function (ACF)
Remember that the ACF of white noise is
Powers are equally distributed at each frequency
Hence the name of ‘white noise’
Colour noise: not equally distributed (ACF is not delta)

## Slide 50
Issues on noise
Remember that the ACF of white noise is
Powers are equally distributed at each frequency
Hence the name of ‘white noise’
Colour noise: not equally distributed (ACF is not delta)
White light passes a prism
White light goes through a prism

## Slide 51
clear all
close all
sampling_rate=100;%Hz
omega=30; %signal frequecy Hz
N=20000; %total number of samples
for i=1:N
x_sound(i)=cos(2*pi*omega*i/sampling_rate); %signal
x(i)=x_sound(i)+2*randn(1,1); %signal+noise
axis(i)=sampling_rate*i/N; % for psd
time(i)=i/sampling_rate; % for time trace
end
subplot(1,2,1)
plot(time,x); %signal + noise, time trace
xlabel('second')
ylabel('x')
subplot(1,2,2)
plot(axis,abs(fft(x)),'r'); % magnitude of signal
xlabel('Hz');
ylabel('Amplitude')
load handel.mat
filename = 'handel.wav';
audiowrite(filename,y,Fs);
clear y Fs
sound(x_sound)
Coming back to Mysterious sound
Fig. 2
noise

## Slide 52
clear all
close all
sampling_rate=100;%Hz
omega=30; %signal frequecy Hz
N=20000; %total number of samples
for i=1:N
x_sound(i)=cos(2*pi*omega*i/sampling_rate); %signal
x(i)=x_sound(i)+2*randn(1,1); %signal+noise
axis(i)=sampling_rate*i/N; % for psd
time(i)=i/sampling_rate; % for time trace
end
subplot(1,2,1)
plot(time,x); %signal + noise, time trace
xlabel('second')
ylabel('x')
subplot(1,2,2)
plot(axis,abs(fft(x)),'r'); % magnitude of signal
xlabel('Hz');
ylabel('Amplitude')
sound(x_sound)
Coming back to Mysterious sound
Fig. 2
noise
signal

## Slide 53: Matlab
A few words on Matlab
periodogram pwelch
It is essentially fft
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
It is slightly advanced

## Slide 54: Matlab
A few words on Matlab
periodogram pwelch
It is essentially fft
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
It is slightly advanced
Abs(fft(x))

## Slide 55: Matlab
Fs = 1000; t = 0:1/Fs:.3;
% Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
periodogram(x,[],'twosided',512,Fs);
% The default window is used
It is slightly advanced
Abs(fft(x))
Fs = 1000; t = 0:1/Fs:.296;
%Fs is the sampling rate
x = cos(2*pi*t*200)+randn(size(t));
% A cosine of 200Hz plus noise
pwelch(x,[],[],[],Fs,'twosided');
% Uses default window, overlap & NFFT.
In Welch, essentially the signals are divided into many segments
For each segments, an FFT is carried
The summation of FFT is plotted and hence the noise is averaged out
A few words on Matlab
periodogram pwelch
It is essentially fft

## Slide 56: Spectrogram
In real life examples, all signals change with time (music for example)

## Slide 57: Spectrogram
In real life example, all signals change with time (music for example)
Using sliding window to sample signals and calculate PSD

## Slide 58: Spectrogram
In real life example, all signals change with time (music for example)
Using sliding window to sample signals and calculate PSD

## Slide 59: Spectrogram
In real life example, all signals change with time (music for example)
Using sliding windows to sample signals and calculate PSD

## Slide 60: Spectrogram
It is called STFT (short time Fourier transform)
The obtained results are plotted using colour map as in the next figure: spectrogram

## Slide 61: Spectrogram
Time (sec)
Frequency
1 Hz
3 Hz

## Slide 62: Example I
t=0:0.001:2; % 2 secs @ 1kHz sample rate
y=chirp(t,100,1,200,'q'); % Start @ 100Hz, cross 200Hz at t=1sec
spectrogram(y,128,120,128,1E3); % Display the spectrogram
title('Quadratic Chirp: start at 100Hz and cross 200Hz at t=1sec');
sound(y)
y=chirp(t,100,1,200,'q'); % Start @
Fs=5000;
filename = 'h.wav';
audiowrite(filename,y,Fs);
Time (sec)
Frequency

## Slide 63: Example II
);
sound(y)
t=0:0.001:20; % 2 secs @ 1kHz sample rate
y=chirp(t,100,1,200,'q'); % Start @ 100Hz, cross 200Hz at t=1sec
spectrogram(y,128,120,128,1E3); % Display the spectrogram
title('Quadratic Chirp: start at 100Hz and cross 200Hz at t=1sec');
Fs=6000;
filename='h.wav';
audiowrite(filename,y,Fs);
Time (sec)
Frequency

## Slide 64: Math
1
T
T
WT[n]
You can certainly choose many ‘windows’ here: triangle, Gaussian, Hamming etc.

## Slide 65: Summary
DFT
Power Spectrum Density
Spectrogram