## Slide 1: DCSP-12: Filter II
Jianfeng Feng
Department of Computer Science Warwick Univ., UK
Jianfeng.feng@warwick.ac.uk
http://www.dcs.warwick.ac.uk/~feng/dcsp.html

## Slide 2: Nonrecursive Filters
When a filter is nonrecursive, its difference equation can be written y(n) = a0 x(n) + a1 x(n-1) +…+ aN x(n-N)
Such filters are also called finite impulse response filters, for the obvious reason that their IR contain only finitely many nonzero terms.
Correspondingly, the TF of a nonrecursive filter can be written as

## Slide 3: Block diagram

## Slide 4
z
Block diagram
a0
a1
aN-1
aN

## Slide 5: Three types of representation
Linear difference equation
Block diagram
Transfer function

## Slide 6: Zeros
Trying to figure out how an MA filter will behave, is not always so simple.
Another way of looking at it is through its frequency domain behaviors.
We can make a start on this by examining the zeros of its transfer function H(z), i.e. those values of z for which
H(z)=0
since H(z) is a polynomial of order N with real
coefficients,

## Slide 7: Zeros
Trying to figure out how an FIR filter will behave, is note always so simple.
Another way of looking at it is through its frequency domain behaviors.
We can make a start on this by examining the zeros of its transfer function H(z), i.e. those values of z for which
H(z)=0
H(z) is a polynomial of order N with real coefficients,
the complex conjugate root theorem states that if P is a polynomial in one variable with real coefficients, and a + bi is a root of P with a and b real numbers, then its complex conjugate a − bi is also a root of P
N =2, H(z) = a0 + a1 z-1 + a2 z-2
the roots of this poly are

## Slide 8: Zeros
We can express H(z) in terms of the roots by writing
where in general
zm= |zm| exp ( j arg [zm] )
is the mth root, or zero of the transfer function.
The zeros of a transfer function are usually denoted graphically in the complex z-plane by circles, as shown in the following Fig.

## Slide 9: Zeros

## Slide 10: Signal

## Slide 11: Recursive Filters
Of the many filter transfer function which are
not MA, the most commonly use in DSP
are the recursive filters, so called because
their current output depends not only on
the last N+1 inputs but also on the last N
outputs.

## Slide 12: Signal

## Slide 13: Frequency Response of an MA filter
We can formally represent the frequency response of the filter by substituting
z = exp( j w)
and obtain
H( w) = K[(exp (-j w) – a1)…(exp (-j w) – aN)]
Consider an example

## Slide 14: What is a Filter?
For a given power spectrum of a signal

## Slide 15: What is a Filter?
For a given power spectrum of a signal
Signal
Filter
1

## Slide 16: What is a Filter?
For a given power spectrum of a signal
1
Filter
Signal
*
Filtered Signal

## Slide 17
Ideal response function as plotted below
Find coefficients a and b
y(n) = a0x(n)+ a1 x(n-1) +…+ aN x(n-N)
+ b1 y(n-1) +…+ bNy(n-N)
1
Filter

## Slide 18
Example
H( w)= K[(exp (-j w) – a1)(exp (-j w) – a2)]
(sampling frequency Fs, stop freqeuncy F0, put zero = (F0/Fs/2)p = 2p F0/Fs)
with a1 = exp (-j p / 4), a2 = exp (j p / 4), for example, then
Y(w)= H( w) X( w)
and Y(w)=0 whenever w = p / 4.
Any signal with a frequency of F0 will be stopped

## Slide 19: Transfer function
h=0.01;
for i=1:314
x(i)=i*h;
f(i)=(exp(-j*x(i))-exp(-j*pi/4))*(exp(-j*x(i))-exp(j*pi/4));
end
plot(x,abs(f))

## Slide 20: Transfer function
Moving a1 along the circle, we are able to stop a signal with a given frequency
p/4
p/3

## Slide 21: Result

## Slide 22: Difference equation
The original difference expression can be recovered by
H( z ) = k [(z-1 – a1)(z-1 – a2)]
= k [z-2 – (a1+ a2 ) z-1 + (a1 a2 )]
y(n) = k [x(n-2) – (a1+ a2 ) x(n-1) + (a1 a2 )x(n)]
a0= k (a1 a2 )=k, a1= – k(a1+ a2 ), a2 = k

## Slide 23: Recursive Filters
Of the many filter transfer function, the most
commonly use in DSP are the recursive filters,
so called because their current output
depends not only on the last N inputs but also
on the last N outputs.
y(n) = a0x(n)+ a1 x(n-1) +…+ aNx(n-N)
+ b1 y(n-1) +…+ bNy(n-N)

## Slide 24
Transfer function

## Slide 25: Block diagram
X(n)
aN
D
D
aN-1
+
a0
y(n)
+
bN
bN-1
a1
b1
+
+
D

## Slide 26: Poles and zeros
We know that the roots an are the zeros of the transfer function.
The roots of the equation B(z)=0 are called the poles of the transfer function.
They have greater significance for the behaviour of H(z): it is singular at the points z = bn.
Poles are drawn on the z-plane as crosses, as shown in the next Fig.

## Slide 27
Poles and zeros

## Slide 28: Poles and zeros
ON this figure, the unit circle has been shown on the z-plane.
In order for a recursive filter to be bounded input bounded output (BIBO) stable, all of the poles of its transfer function must lie inside the unit circle.
A filter is BIBO stable if any bounded input sequence gives rise to a bounded output sequence.
Now if the pole of the transfer lie insider the unit circle,
A simple case (N=1)

## Slide 29: Poles and zeros
y(n) is stable if and only if the pole is inside the unit circle
|b|<1
In general, y(n) is stable is stable if and only if all poles are inside
the unit circle
|bi|<1, i=1,..,N

## Slide 30: Poles and zeros
If |bi |=1, the filter is said to be conditionally stable:
some input sequence will lead to bounded output sequence and some will not.
Since MA filters have no poles, they are always
BIBO (bound input bound output) stable: zeros
have no effect on stability.

## Slide 31: Response
Now suppose we have the transfer function of a filter
We can formally represent the frequency response of the filter by substituting
z = exp( j w)
and obtain
H( w)= A( w ) / B( w )

## Slide 32: Response
Obviously, H( w) depends on the locations of the poles and zeros of the transfer function, a fact which can be made more explicit by factoring the numerator and denominator polynomials to write

## Slide 33: Response
Each factor in the numerator or denominator is a complex function of frequency, which has a graphical interpretation in the terms of the location of the corresponding roots in relation to the unit circle
Thus we can make a reasonable guess about the filter frequency response imply by looking at the pole-zero diagram.

## Slide 34: Filter Types
There are four main classes of filter in widespread use:
filters.
The name are self-explanatory
This four types are shown in the next figure
Lowpass
highpass
bandpass
bandstop

## Slide 35: Filter Types