## Slide 1
Seminar 6 Digital Communication and Signal Processing
Ruohan Zhang
Ruohan.Zhang.1@warwick.ac.uk
Department of Computer Science, University of Warwick
26/02/2024

## Slide 2
Exercise 1
The typical syntax for computing the FFT of a signal is FFT(x), where x is the signal x[n] that you wish to transform. Try to generate a signal as you like, plot it out, try FFT, and plot it out in frequency domain.
Key points:
In sampling, , where sampling rate means the number of sampling points in a second.
2. We can generate a signal in time domain like . If we change some of the parameters in this signal. In this way, we will get another new signal.
3. In MATLAB, the function fft( ) is used to change the signal from the time domain to the frequency domain.

## Slide 3
Exercise 2
Load the data “handel” in matlab. This data is a piece of music signal.
1) Try to plot this signal in the time domain.
2) Transform this signal by using FFT and plot this signal in the frequency domain.
3) Try to work out the spectrogram.
4) Why not try to add some noise to this signal? for example, noise at 1000HZ or 2000HZ, or even a white noise? And then plot this noised signal as 1), 2), 3) and compare with the original one.
Key points:
A spectrogram is a visual representation of the spectrum of frequencies of a signal as it varies with time.
Noise at 1000Hz or 2000Hz means the frequency of the noise signal is 1000Hz or 2000Hz.