## Slide 1: A CUDA Implementation of the HPCG Benchmark
Everett Phillips
Massimiliano Fatica

## Slide 2: outline
Introduction
CUDA Implementation
Optimization
Performance Results
  Single GPU
  GPU Supercomputers
Conclusion
High Performance Conjugate Gradient Benchmark

## Slide 3: Why HPCG ?
Supercomputer Ranking / Evaluation
Dense Linear Algebra (Ax = b)
Compute intensive
  DGEMM (Matrix-Matrix Multiply)
  O(N3)FLOPS / O(N2) Data
  10-100 Flop/Byte
Workload does not correlate with many modern applications
HPL (Linpack) Top500 benchmark

## Slide 4: Why HPCG?
New Benchmark to Supplement HPL
Common Computation Patterns not addressed by HPL
Numerical Solution of PDEs
Memory Intensive
Network

## Slide 5: HPCG Benchmark
Preconditioned Conjugate Gradient Algorithm
  Sparse Linear Algebra (Ax = b), Iterative solver
  Bandwidth Intensive: 1/6 Flop/Byte
Simple Problem (sparsity pattern of Matrix A)
  Simplifies matrix generation/solution validation
  Regular 3D grid, 27-point stencil
  Nx x Ny x Nz local domain / Px x Py x Pz Processors
  Communications: boundary + global reduction

## Slide 6: HPCG ALGORITHM
Multi-Grid Preconditioner
  Symmetric-Gauss-Seidel Smoother (SYMGS)
Sparse Matrix Vector Multiply (SPMV)
Dot Product – MPI_Allreduce()

## Slide 7: HPCG BENCHMARK
  Problem Setup – initialize data structures
  Optimization (required to expose parallelism in SYMGS smoother)
    Matrix analysis / reordering / data layout
    Time counted against final performance result
  Reference Run – 50 iterations with reference code – Record Residual
  Optimized Run – converge to Reference Residual
    Matrix re-ordering slows convergence (55-60 iterations)
    Additional iterations counted against final performance result
    Repeat to fill target execution time (few minutes typical, 1 hour for official run )

## Slide 8: HPCG
Exchange_Halo(x) //neighbor communications
for row = 0 to nrows
sum  0
for j = 0 to nonzeros_in_row[ row ]
col  A_col[ j ]
val  A_val[ j ]
sum  sum + val * x[ col ]
y[ row ]  sum
No dependencies between rows, safe to process rows in parallel
SPMV (y = Ax)

## Slide 9: HPCG
Exchange_Halo(x) //neighbor communications
for row = 0 to nrows (Fwd Sweep, then Backward Sweep for row = nrows to 0)
sum  b[ row ]
for j = 0 to nonzeros_in_row[ row ]
col  A_col[ j ]
val  A_val[ j ]
if( col != row ) sum  sum – val * x[ col ]
x[ row ]  sum / A_diag[ row ]
if col < row, must wait for x[col] to be updated
SYMGS (Ax = y, smooth x)

## Slide 10: CUDA IMPLEMENTATIONS
Cusparse CSR
Cusparse CSR + Matrix Reordering
Custom Kernels CSR + Matrix Reordering
Custom Kernels ELL + Matrix Reordering

## Slide 11: BASELINE Cusparse
Leverage existing Libraries
  CUSPARSE (TRSV + SPMV), CUBLAS (DOT, AXPY), THRUST (sort, count)
  Flexible, works with any matrix ordering (allows experimentation)
Shortcomings
  Triangular solve perf (limited parallelism, memory access pattern)
  Expensive Analysis for Triangular Solves
  Extra steps to compute SYMGS ( SPMV + Vector Update)
  Columns must be sorted WRT diagonal

## Slide 12: OptimizED versions
Reorder Matrix (Graph Coloring)
  triangular solve perf
Custom Kernels
  Removes extra steps in SYMGS (same algorithm as reference)
  No cusparse analysis overhead
  Relaxed data format requirements (non square mtx and unsorted columns ok)
ELLPACK
  Memory access efficiency

## Slide 13: Matrix Reordering (Coloring)
SYMGS - order requirement
  Previous rows must have new value
  reorder by color (independent rows)
  2D example: 5-point stencil -> red-black
  3D 27-point stencil = 8 colors

## Slide 14: Matrix Reordering (coloring)
Coloring to extract parallelism
Assignment of “color” (integer) to vertices (rows), with no two adjacent vertices the same color
“Efficient Graph Matching and Coloring on the GPU” – (Jon Cohen)
  Luby / Jones-Plassman based algorithm
  Compare hash of row index with neighbors
  Assign color if local extrema
  Optional: recolor to reduce # of colors

## Slide 15: More Optimizations
Overlap Computation with neighbor communication
Overlap 1/3 MPI_Allreduce with Computation
__LDG loads for irregular access patterns (SPMV + SYMGS)

## Slide 16: Optimizations
SPMV Overlap Computation with communications
Gather to GPU send_buffer Copy send_buffer to CPU MPI_send / MPI_recv Copy recv_buffer to GPU Launch SPMV Kernel
Time
GPU
CPU

## Slide 17: Optimizations
SPMV Overlap Computation with communications
Gather to GPU send_buffer Copy send_buffer to CPU Launch SPMV interior Kernel MPI_send / MPI_recv Copy recv_buffer to GPU Launch SPMV boundary Kernel
Time
GPU Stream A
GPU Stream B
CPU

## Slide 18: RESULTS – Single GPU

## Slide 19: RESULTS – SINGLE GPU

## Slide 20: RESULTS – SINGLE GPU

## Slide 21: RESULTS – SINGLE GPU

## Slide 22: RESULTS – GPU SUPERCOMPUTERS
Titan @ ORNL
  Cray XK7, 18688 Nodes
  16-core AMD Interlagos + K20X
  Gemini Network - 3D Torus Topology
Piz Daint @ CSCS
  Cray XC30, 5272 Nodes
  8-core Xeon E5 + K20X
  Aries Network – Dragonfly Topology

## Slide 23: RESULTS – GPU SUPERCOMPUTERS
1 GPU = 20.8 GFLOPS (ECC ON)
~7% iteration overhead at scale
Titan @ ORNL
  322 TFLOPS (18648 K20X)
  89% efficiency (17.3 GF per GPU)
Piz Daint @ CSCS
  97 TFLOPS (5265 K20X)
  97% efficiency (19.0 GF per GPU)

## Slide 24: Results – GPU SUPERCOMPUTERS
DDOT (-10%)
  MPI_Allreduce()
  Scales as Log(#nodes)
MG (-2%)
  Exchange Halo (neighbor)
SPMV (-0%)
  Overlapped w/Compute

## Slide 25: Reproducibility
Residual Variance (reported in output file)
  zero = deterministic order of floating point operations
GPU Supercomputers bitwise reproducible up to full scale
  except with network hardware-acceleration enabled on Cray XC30
Parallel Dot Product
  Local GPU routines bitwise reproducible
  MPI_Allreduce()
    reproducible with default MPI implementation
    Non-reproducible with network offload (hardware atomics)

## Slide 26: Reproducibility
CRAY XC30 MPI_Allreduce()
  Default  reproducible results but lower performance
    Min MPI_Allreduce time: 0.0296645 Max MPI_Allreduce time: 0.153267 Avg MPI_Allreduce time: 0.0916832
  MPICH_USE_DMAPP_COL=1
    Min DDOT MPI_Allreduce time: 0.0379143 Max DDOT MPI_Allreduce time: 0.0379143 Avg DDOT MPI_Allreduce time: 0.0379143
    Residuals: 4.25079640861055e-08 4.25079640861032e-08 4.25079640861079e-08 4.25079640861054e-08

## Slide 27: Supercomputer Comparison

## Slide 28: Power Consumption
Piz Daint (5208 K20X)
  99 TF / 1232 kW
  0.080 GF/W
GK20A (Jetson TK1)
  1.4 GF / 8.3 Watts
  0.168 GF/W

## Slide 29: CONCLUSIONS
GPUs proven effective for HPL, especially for power efficiency
  High flop rate
GPUs also very effective for HPCG
  High memory bandwidth
  Stacked memory will give a huge boost
Future work will add CPU + GPU

## Slide 30: Acknowledgments
Oak Ridge Leadership Computing Facility (ORNL)
  Buddy Bland, Jack Wells and Don Maxwell
Swiss National Supercomputing Center (CSCS)
  Gilles Fourestey and Thomas Schulthess
NVIDIA
  Lung Scheng Chien and Jonathan Cohen