## Slide 1: Roofline Model Toolkit : A Practical Tool for Architectural and Program Analysis
Yu Jung Lo*, Samuel Williams†, Brian Van Straalen†, Terry Ligocki†, Matthew Cordery†, Nicholas Wright†, Mary Hall*, Leonid Oliker†
*University of Utah † Lawrence Berkeley National Laboratory
yujunglo@cs.utah.edu

## Slide 2
Motivation
Performance Model
Architecture Characterization
Application Performance Measurement
Hard to find technical specs for most HPC platforms to form “textbook” Roofline model.
Even with technical specs, the real issue is achievable performance.
Issues
Empirical benchmark-driven Roofline model

## Slide 3
“Theoretical” Roofline Model
Peak Memory Bandwidth
Peak FP Performance
Gflop/s = min

## Slide 4
Micro Benchmarks
int main () { #pragma omp parallel private(id) { uint64_t n, t; initialize(&A[nid]); for (n = 16; n < SIZE; n *= 1.1) { for (t = 1; t < TRIALS; t *= 2) { // start timer here Kernel(n, t, &A[nid]); // stop timer here #pragma omp barrier #pragma omp master { MPI_Barrier(MPI_COMM_WORLD); }
}}}
void Kernel (uint64_t size, unit64_t trials, double * __restrict__ A) { double alpha = 0.5; uint64_t i, j; for (j = 0; j < trials; ++j ) { for (i = 0; i < nsize; ++i) { A[i] = A[i] + alpha; } alpha = alpha * 0.5; }}
Driver
Bandwidth
double bytes = 2 * sizeof(double) * (double)n * (double)t;
Sync
Init
Compute

## Slide 5
Micro Benchmarks (cont’)
int main () { #pragma omp parallel private(id) { uint64_t n, t; for (n = 16; n < SIZE; n *= 1.1) { for (t = 1; t < TRIALS; t *= 2) { // start timer here Kernel(n, t, &A[nid]); // stop timer here #pragma omp barrier #pragma omp master { MPI_Barrier(MPI_COMM_WORLD); }
}}}
void Kernel (uint64_t size, unit64_t trials, double * __restrict__ A) { double alpha = 0.5; uint64_t i, j; for (j = 0; j < trials; ++j ) { for (i = 0; i < nsize; ++i) { double bete = 0.8; #if FLOPPERITER == 2 beta = beta * A[i] + alpha; #elif FLOPPERITER == 4 … #endif A[i] = beta; } alpha = alpha * 0.5; }}
Driver
GFlops
double bytes = FLOPPERITER * (double)n * (double)t;
Compute

## Slide 6
Architectural Platforms
Edison (Intel Xeon CPU)
Mira (IBM Blue Gene/Q)
Babbage (Intel Xeon Phi)
Titan (Nvidia K20x)

## Slide 7
Bandwidth Benchmark Results
Edison (Intel Xeon CPU)
Mira (IBM Blue Gene/Q)
Babbage (Intel Xeon Phi)
Titan (Nvidia K20x)
1 MB

## Slide 8
Bandwidth Benchmark Results (cont’)
dim3 gpuThreads(64); dim3 gpuBlocks(224); // start timer here
#if defined (GLOBAL_TRIAL_INSIDE)
global_trialInside <<<gpuBlocks, gpuThreads>>> (nsize, trials, d_buf);
#elif defined(GLOBAL_TRIAL_OUTSIDE)
for (uint64_t t = 0; t < trials; ++t) {
global_trialOutside <<<gpuBlocks, gpuThreads>>> (nsize, d_buf, alpha); alpha = alpha * (1 – 1e-8); }
#else
sharedmem <<<gpuBlocks, gpuThreads>>> (nsize, trials, d_buf);
#endif
cudaDeviceSynchronize();
// stop timer here
(blocks, threads)
Titan (Nvidia K20x)
A
B
C

## Slide 9
Optimized GFlops Benchmarks
double alpha = 0.5; for (j = 0; j < ntrials; ++j ) { for (i = 0; i < nsize; ++i) { double bete = 0.8; beta = beta * A[i] + alpha; A[i] = beta; } alpha = alpha * (1e-8); }
for (j = 0 ; j < ntrials; ++j) { for (i = 0 ; i < nsize ; i += 8) { bv1 = _mm256_set1_pd(0.8); v1 = _mm256_load_pd(&A[i]); bv1 = _mm256_mul_pd(bv1, v1); bv1 = _mm256_add_pd(bv1, v1); _mm256_store_pd(&A[i], bv1); // repeat above operations for A[i+4] } alpha = alpha * (1e-8); av = _mm256_set1_pd(alpha); }
for (j = 0 ; j < ntrials ; ++j){ for (i = 0 ; i < nsize ; i += 8){ bv1 = vec_splats(0.8); v1 = vec_ld(0L, &A[i]); bv1 = vec_madd(bv1,v1,av); vec_st(bv1, 0L, &A[i]); // repeat above operations for A[i+4] } alpha = alpha * (1e-8); vec_splats(alpha); }
for (j = 0 ; j < ntrials ; ++j) { for (i = 0 ; i < nsize ; i += 8) { bv1 = _mm512_set1_pd(0.8); v1 = _mm512_load_pd(&A[i]); bv1 = _mm512_fmadd_pd(bv1,v1,av); _mm512_store_pd(&A[i], bv1); } alpha = alpha * (1e-8); av = _mm512_set1_pd(alpha); }
C Code
AVX Code (Edison)
QPX Code (Mira)
AVX-512 Code (Babbage)
2 Flops per Element
Unroll by 8
Fused Multiply & Add
Fused Multiply & Add

## Slide 10
Gflops Performance
Edison (Intel Xeon CPU), 8 FPE
Mira (IBM Blue Gene/Q), 16 FPE
Babbage (Intel Xeon Phi), 16 FPE
Theoretical Peak
Turbo Boost
Optimized code
C code
256 FPE, SIMD and unrolled by 16

## Slide 11
Gflops Performance (cont’)
Edison (Intel Xeon CPU)
Mira (IBM Blue Gene/Q)
Babbage (Intel Xeon Phi)
Titan (Nvidia K20x)

## Slide 12
Beyond the Roofline

## Slide 13
CUDA Unified Memory
Unified Memory
Unified Virtual Addressing (UVA)
Pageable Host
with Explicit Copy
Page-locked Host
with Explicit Copy
Page-locked Host
with Zero Copy
Unified Memory
with Zero Copy
Separate Address Spaces
CUDA’s Memory Concept
Four Approaches to Manage Memory
1
2
3
4
Explicit Copy
Implicit Copy

## Slide 14
CUDA Managed Memory Benchmark
int main() { // start timer here… for (uint64_t j = 0; j < trials; ++j) {
for (uint64_t k = 0; k < reuse; ++k) { GPUKERNEL <<<blocks, threads>>> (n, d_buf, alpha); alpha = alpha * (1e-8); }
CPUKERNEL(n, h_buf, alpha); } // stop timer here… double bytes = 2 * sizeof(double) * (double)n * (double)trials * (double)(reuse + 1); }
#if defined(_CUDA_ZEROCPY) || defined(_CUDA_UM) cudaDeviceSynchronize();
#else cudaMemcpy(d_buf, h_buf, SIZE, cudaMemcpyDefault); #endif
#if defined(_CUDA_ZEROCPY) || defined(_CUDA_UM) cudaDeviceSynchronize();
#else cudaMemcpy(h_buf, d_buf, SIZE, cudaMemcpyDefault); #endif
1
2
4
3
K iterations
K + 1 iterations

## Slide 15
CUDA Managed Memory Performance
* GPU driver version: 331.89; toolkit version: 6.0beta
Pageable host w/ explicit copy
Page-locked host w/ explicit copy
Page-locked host w/ zero copy
Unified Memory w/ zero copy
1
2
4
3
156 GB/s
128 GB/s

## Slide 16
Construct the Roofline Model

## Slide 17
Empirical Roofline Model
Edison (Intel Xeon CPU)
Mira (IBM Blue Gene/Q)
Babbage (Intel Xeon Phi)
Titan (Nvidia K20x)

## Slide 18
Application Analysis : MiniDFT
Flat MPI
MPI tasks x OpenMP threads

## Slide 19
Conclusion
Way to get high bandwidth on manycore and accelerated architectures.
  Massive parallelism on large working sets.
Way to get high Gflops
  Sufficient SIMDized and unrolled.
  At least 2 threads per core for in-order processor.
  High FPE for manycore and accelerators.
Way to get high CUDA managed memory performance
  Highly reuse the data on device, operate on large working set, and explicit copy between host and device.

## Slide 20
Questions?

## Slide 21
Appendix

## Slide 22
Appendix